## Slide 1: 3D printing: Applications Overview
Yehuda Rozilyo

## Slide 2: Intro to 3D Printing
A process for making 3D products by primarily adding material rather than removing it. It has become synonymous with 3D printing.

## Slide 3: Intro to 3D Printing
2D Vs. 3D Printing = Moveable Tray

## Slide 4: Industry’s “biggest problem”
One Solution = Unavailable
SLA
FDM
SLS
DMLS
EBM
BJ
MJ
Poly Jet

## Slide 5: 3D Printing: Practical Industry Applications
Focus on Top 3 technologies: FDM, PolyJet (SLA), SLS

## Slide 6: Who Use It?
  Footwear
  Toys
  Dental
  Architecture
  Animation &
  Entertainment
  Consumer electronics
  Consumer goods
  Aerospace & defense
  Automotive
  Medical & medical equipment
Notes: We will review more examples as we go along

## Slide 7: Hollywood: Printing Examples

## Slide 8: Testing | Form, fit and function
The prototype can be properly tested and checked for design faults early on in the design cycle.
Once a design fault is identified in the model, designers and engineers can simply tweak the design on the CAD/CAM
The electronics and mechanical elements fitted into the printed part

## Slide 9: Testing | Ergonomics
Examine how people interact with a product
Prototyping is essential since physical properties significantly impact ergonomic performance, a 3D CAD model is not sufficient
A combination of elastomeric materials and rigid materials allow for ergonomics studies to take hold
Understanding grip and handling suitable for the working environment

## Slide 10: Marketing | Focus Groups, Exhibitions and Sales tools
Present future products in early stages of the design
Get customers’ feedback on new products before production
Exhibit prototype models to show future products expected to come out in the near future without much cost incurred

## Slide 11: Marketing | Graphic Design & Package
Once product development is complete…..
Use the prototype as models for packaging rather than wait for pre-series production parts
“print reality” – producing models that have the same “look & feel” as the end product
Model printed with FullCure720 and painted with Acrylic-Paint
Notes: These prototypes are printed on Stratasys PolyJet 3D printer, and, together with post-processing such as painting, metal coating, and more, create the look-and-feel of the end product.

## Slide 12: Over Molding
Two or more materials are combined to produce a single part, typically a rigid plastic with a rubber-like elastomeric material
Applications for over molding include non-slip grips & handles, shock absorption, vibration reduction, multi-colored components, weather proofing and aesthetic enhancement.
Production Part
Printed Parts
Notes: Connex rigid & rubber-like combination is perfect for over molding

## Slide 13: Labeling & Texturing
Branding, labels and textural elements allow to differentiate models, visualize end products and appreciate product aesthetics.
Closer resemblance to the end product
Notes: Texturing is primarily used for visualization, appearance and rendering purposes. It’s also allows product differentiation and customization
Labeling allows for product recognition to be part of the product design, as well as for a closer resemblance to the end product

## Slide 14: Impact Resistance
Parts can be coated using a different materials to generate impact resistance. Various coating determinations allow for different resistance levels
Simulates behavior of part on strong impact
Drop tests are used to determine impact resistance
Notes: Nimrod Car is a good example of how Connex DM materials can be used to provide good impact resistance. The car races at 40 km/h on rough terrain and doesn’t break!

## Slide 15: Gaskets Plugs & Seals
A gasket is a mechanical seal that fills the space between two mating surfaces, generally to prevent leakage from or into the joined objects while under compression
Plugs and Seals are used by printing by combining both rigid and rubber materials in single build
Improve sealing by coating parts with rubber materials

## Slide 16: Dynamic Friction
Kinetic (or dynamic) friction occurs when two objects move relative to each other and rub together
Variety of rubber and rigid materials, each has its unique coefficient of friction.
Mix rigid and rubber materials in the same part creating a greater range of friction coefficients.
The Bio Snake robot Case Study
Material B
Material A
Material C
Material D
Notes: The Bio snake robot case study is a great example
If we zoom into one link of the bio snake robot, one can clearly see that this link has a unique structure.
Each color represents a separate shell, while for each shell a different material is applied.
When the bio snake robot moves forward, the surface meets material B (Rigid, VeroWhitePlus and TangoBlackPlus)
When it tries to move backwards it meets material A (shore A 40 a combination of VeroWhitePlus and TangoBlackPlus)
Facilitates the movement forward

## Slide 17: Tooling Applications | Injection Molding
Injection molding is the most commonly used manufacturing process for producing high precision, complex plastic parts.
Printing the mold using 3D Printing allows:
  Short series production
  Prototyping from the real plastic material
  Drastically reduced time and costs

## Slide 18: Tooling Applications | Blow Molding
The advantages of printing a 3D Printed mold:
Drastically reduce time and costs
Ideal solution for small series production
The printed mold can be assembled onto conventional blow molding machines
Prototyping from the actual thermoplastic material - PP, PE, PET
Allow for mechanical evaluation
Customization of design - logos, text, pictures easily incorporated

## Slide 19: Tooling Applications | Silicon Molding
Also known as: RTV Molding, Vacuum Casting, Urethane Casting, Soft Tooling
Used for short series production
3D Printed part is used as a master pattern
Why 3D Printing:
  Smooth surface (critical)
  Fine details
  Good HDT for silicone molding
  Time & Money

## Slide 20: 3D Printing: Industry Case Studies
Focus on: Defense, Communication, Medical, Automotive, Research

## Slide 21: Defense| exploration
A.I Drones
Hand-held-Scanner
Requirements: Durable, high HDT, Movable, Low degradation rate.

## Slide 22: Defense | Aerospace
Fiber reinforced (composite) application
Master Part
Mold

## Slide 23: (Basic proof of concept for all drone manufacturing)
UAV\Drones
Requirements: UV resistance, Durable,
Light, High HDT
Defense | Aerospace

## Slide 24: Defense | Aerospace
UAV\Drones
Requirements: UV resistance, Durable, Light, High HDT, Adjustable (Lego Mode)

## Slide 25: Defense\Medical | Respirator
Respirator prototype
Requirements: changeable parts (Lego mode), rigid to flexible materials selection, unified color, clear usable lenses.

## Slide 26: Medical | Surgical Planning & Surgical Guides
Surgical Planning- models can be printed from 3D generated s/w solutions resting on MRI, CTI or US platforms
Surgical guides- prepare a guide that will help you better understand where you can place your implants
To hold jaw in place, rods need to be placed at exact angle
Surgical guide designed to determine these angles
Medical surgeons consulting prior to an operation
Notes: Surgical Guides example- You can see here a customized guide is being prepared for a patient whose jaw is broken.
The key to this guide is in understanding the angles at which these rods will go into the patient’s skull.
It is the angles here that play a crucial role and doing this prior to operation saves a lot of time and possible mistakes

## Slide 27: Medical | Surgical Planning & Surgical Guides
Medical
Printing a skull model with rigid materials for surgery planning
  Scan by CT/MRI and convert to STL
  Print a skull and a missing plate
Notes:   Produce a very accurate plate based on the model and reduce the surgery time significantly

## Slide 28: Medical | Research
Research into the origins of human morphology and behavior
Printing highly accurate replica of a fossil skull for research purposes in the Anthropological Institute at Zurich University
Notes: Parts were printed on Eden250
The printed models enabled researchers to gain new insights into female Neanderthals’ anatomical structures, Neanderthal brain size evolution and other aspects of the history of human evolution
Parts were printed on Eden250

## Slide 29: Medical | Dental (Surgical Guides & temp implants )
3D Printed Surgical Guides provides Implants with Digital Precision
Requirements: Bio-Compatible, life-like Color scheme, sustainable

## Slide 30: Communication | Dashboard
Flexible\Adjustable Dashboard
Requirements: High shore value,
Semi-rigid, Snap-fit capabilities,
UV resistance.
Overnight print

## Slide 31: Automotive | lighting assessment
Clear parts are used for lighting assessment
Requirements: high HDT, Durable, UV resistance, Clear.
Medcal

## Slide 32: Communication | Case Study
The Robotic Scanner is a patent pending device which learns when and where to focus its attention; directing room scanning location toward regions of the body which most affect comfort.
(Image by Andrew Payne. All rights reserved)
Notes: The accuracy of the printer combined with the strength of the Digital ABS enabled precisely fitting mechanical connections, like screw threads and friction-fit fasteners, to be printed directly into the parts.
Designed by Andrew Payne is a registered architect and inventor who is currently pursuing his doctoral degree at Harvard’s Graduate School of Design.
The device has three internal motors which move the fan left-to-right and up-and-down to achieve maximum personalized comfort. The fan consumes about one third of the power of a traditional desk fan.

## Slide 33: Consumer Goods | Case Study
Functional Hot Water Testing
Requirements: Move functional testing to the early stage of concept design
Full functionality, no deformation

## Slide 34: Microfluidic Chambers
Microfluidic chips: small volume, low energy consumption
Requirements: small volume(16 microns per layer),
sustain aggressive liquids, easy post-process

## Slide 35: Limitless Possibilities
3D printing = “You are Only Limited by Your Imagination”

## Slide 36: Thank You
Yehuda Rozilyo