## Slide 1
מהמעבדה לשטח – אינטגרציה, בדיקות והטמעה
סרגיי טוזיק
Verification, Validation and Safety of Autonomous Vehicles
Yoav Hollander, Foretellix ltd

## Slide 2: Introduction - what I’ll discuss in this presentation
The current state of ADS V&V (and safety)
  Why it is so important, and yet so hard to do
What my company (Foretellix) is doing about it
  And how we got here
How this relates to V&V of other autonomous systems
  Autonomous ships, drones, assistive robots and so on
Consider this an informal briefing
  V&V: Verification and Validation
  ADS: Autonomous Driving Systems, including
    AV: Autonomous Vehicle
    ADAS: Advanced Driver Assistance System

## Slide 3: Agenda
Why ADS V&V is hard
Introducing Foretellix
Coverage-Driven Verification
Safety

## Slide 4: Agenda
Why ADS V&V is hard
Introducing Foretellix
Coverage-Driven Verification
Safety

## Slide 5: Current state of AVs
Everybody knows the “big disruption” is coming
  Companies have spent many billions on dollars on this
Real, full-scale autonomy is harder than expected
  So many companies are going after the “easier” verticals first
The main problem is V&V
  Behavior space is huge (and can’t be verified formally)
  No clear decision of “what’s enough”

## Slide 6: The challenges of ADS V&V
Most Complicated System
6
150M Lines of Code
>100’s Chips
Millions of Scenarios
The Infinity challenge
Several Machine Learning Systems
Most Complex Environment
=
ADS
Unpredictable
Actors
Human
Drivers
Cyclists
Pedestrians
Roads
Weather
AVs are less complicated than (say) nuclear submarine, but:
There will to be millions of AVs, with no trained operators

## Slide 7: V&V basics
As V&V people, our job is to help the organization
  Find bugs, measure progress, demonstrate safety
Bugs can kill
  Projects, careers, people
We need to target both “expected” and “unknown” issues
  And risk dimensions are an excellent way to start
Historically, automotive people were not SW people
  So they assumed they can think of all possible issues
  So were pretty bad at looking for the SOTIF “unsafe unknowns”
Everybody is struggling with the “long tail” issue
  Coverage Driven Verification (+extensions) are the best way of handling this
“Expected” issue: Speed-on-snow too high (wrong-setting bug)
Unknown issue:
Ariane 5 blowing up
(SW bug)
Unknown issue: Unconsidered situation (spec bug)
See post about spec bugs
  SOTIF: Safety Of The Intended Function (a standard)

## Slide 8: Handling multiple risk dimensions
Risk dimensions (as a coverage plan)
ODD-edge issues
Arbitrary subsystem failures
Interactions with other AVs
Production / maintenance variability
Behavior during / after accidents
…
Mixing any of the above
Driving scenarios
Topology
Locale
Weather
Other participants
Emergency situations
Human behavior
ML limitations
Locale change
Mode confusions
Sensing issues
Planning issues
Verification system
Monitoring / coverage collection
Grading
Planning / execution
SW
simulation
HIL
VeHIL
Test
track
Street
driving
Abstract
scenarios
Coverage
+ grades
  ODD: Operational Design Domain (where the ADS can drive)

## Slide 9: Agenda
Why ADS V&V is hard
Introducing Foretellix
Coverage-Driven Verification
Safety

## Slide 10: About Foretellix
We create tools and methodologies to help others perform V&V
Including a scenario description language which is now a standard
  ASAM OpenSCENARIO 2.0
Including tools for executing this language
  With any simulator
  While doing checking and collecting coverage
Including scenario libraries, methodology, …
See OSC2 standard release candidate
See web site

## Slide 11: Example scenario: cut_in_and_slow()
Phase 1: Green car accelerating
Phase 2: Green car changing lanes
Phase 3: Green car slowing down
Parameters:
From which side
Speed of EGO
Relative speed of green car
Cut in aggressiveness
Deceleration rate
Number of lanes
Road topology
…
scenario dut.cut_in_and_slow:
car1: car # The other car
side: side_left_right # A side: left or right
do serial:
phase_1: parallel(duration: in [1..5]s):
ego.drive() with:
speed([30..70]kph)
car1.drive() with:
position([5..100]m, behind: ego,at: start)
position([5..15]m, ahead_of: ego, at: end)
phase_2: parallel(duration: in [2..5]s):
ego.drive()
car1.drive() with:
lane(side_of: dut.car, side: side, at: start)
lane(same_as: dut.car, at: end)
phase_3: parallel(duration: in [1..5]s):
dut.car.drive()
car1.drive() with:
change_speed(-[10..15]kph)
AV

## Slide 12
OSC2 scenario definitions are abstract
  One definition can be run with many seeds, resulting in different parameters, locations etc.
All right reserved – Foretellix 2019 ©
Resulting scenario runs

## Slide 13: Scenario composition: Mixing
Create many more meaningful scenarios and extend your coverage by mixing and overlaying different scenarios
Create Combinations of Combinations of edge cases and scenarios a human cannot think about
Use a proven methodology together with innovative ML to improve coverage of critical safety metrics
All right reserved – Foretellix 2019 ©
scenario sut.mix_dangers:
do parallel:
cut_in_and_slow()
interceptor_at_yield()
weather(rain)
Mixing scenarios

## Slide 14
Create many more meaningful scenarios and extend your coverage by mixing and overlaying different scenarios
Create Combinations of Combinations of edge cases and scenarios a human cannot think about
Use a proven methodology together with innovative ML to improve coverage of critical safety metrics
All right reserved – Foretellix 2019 ©
scenario sut.mix_dangers:
do parallel:
cut_in_and_slow()
interceptor_at_yield()
weather(rain)
Resulting scenario runs

## Slide 15: Foretellix also offers
Tools to aggregate / analyze results
V&V packages
Debug tools
Checking constructs
Optimizers + framework
Methodology / consulting
AV
Oncoming Traffic
Speed Limit Change
AV
50
Deceleration
AV
Lane hugger
AV
Follow
AV
Environmental
AV
Lane End
AV
Stopped Vehicles
AV
Merge (heavy traffic)
AV
Merge (high speed)
AV
On Ramp
AV
Cut-out to offramp
AV
AV
Approach
Change Lane
AV
Cut in
AV
Cut-out with brake
AV
Encroaching Oncoming
AV
Cut out
AV
Double Cut-in
AV
…

## Slide 16: Agenda
Why ADS V&V is hard
Introducing Foretellix
Coverage-Driven Verification
Safety

## Slide 17: Coverage Driven Verification (CDV)
What is Coverage?
  Coverage measures “what we have tested so far” (which scenarios, with which parameters, …)
  Breaks the infinite test space into a large-but-finite set of “buckets”
  Assures that each bucket was exercised “enough” by some test(s)
Why use CDV?
  To deal with infinite number of scenarios in a measurable and efficient way
  To explore and cover the test space at massive scale with minimal human intervention
  To discover unknowns, and edge cases
Coverage vs. KPIs / checks
  Coverage measures how well you tested
  KPIs and checks measure how well the SUT behaved in those tests
  KPI: Key Performance Indicator
  SUT: System Under Test
See post about CDV
Parameters:
From which side
Speed of EGO
Relative speeds
Cut in aggressiveness
Deceleration rate
Number of lanes
Road topology
…

## Slide 18: Handling risk dimensions
How to look for unknowns
  Mix risk dimensions
  Monitor recordings for surprises
  Quickly add (and generalize) new things
Use risk dimensions, not just requirements, as scenario sources
  As you find issues, you may add new requirements
Risk dimensions are more inclusive: can come from
  Requirements
  Experience, accident databases, common sense
  Developer hints (including whitebox information)
  …
When in doubt, add more
  Don’t worry about overlap

## Slide 19: Going from 1K runs to 100K/1M runs
For 1K runs
  You carefully select and justify each test
  You know how you’ll check each test
For 1M runs, you need to adopt a different methodology (CDV)
  To remove the new roadblocks to productivity, you need:
Easy ways to plan / create / track many meaningful runs
  Lots of randomization, and easy ways to compose and mix stuff
  Coverage metrics to define the goals and track what you did
Flexible, efficient ways to do automatic checking and KPI collection
  Including adaptable threshold, global / per-scenario checks, and so on
Flexible, efficient methodology / tools to debug (potential) errors and gray areas
  Run-time / post-run verdict analysis
  Interactive multi-run query / analysis tools
  Single-run debug, …
Enhance
content
Run test suite
Do triage / debug
Fix / enhance SUT
Analyze coverage
Notes: Add visual inspection

## Slide 20: Agenda
Why ADS V&V is hard
Introducing Foretellix
Coverage-Driven Verification
Safety

## Slide 21: ADS project milestones
Development
timeline
First integration
First demo
5-vehicle limited pilot
10..100 vehicle pilot
1k..10k limited deployment
100k deployment
OTA updates
Safety-related
timeline
First fatal accident
First trial / investigation
1..8 months
(100K vehicles * 40k km/year * 1 fatality / Bkm = 4 fatalities / year)
Regulatory milestones
The customer is usually here when we meet
Removing dangerous bugs efficiently
guided by milestones
Estimating / minimizing residual risk
guided by the safety argument
Time
Risk
  OTA: Over The Air

## Slide 22: Example: Avoiding “tradeoff bugs” (the role of probabilities)
Emergency braking threshold
Risk estimate for this threshold
Optimal value
for Sweden
Optimal value
for India
Brake earlier
Brake later
V1
Ego
When should the green car start emergency braking?
Note: Similar statistical considerations apply to safety, productivity and more

## Slide 23: Summary
ADS V&V (and safety) are really hard
  But really important
The automotive industry is going through a disruption
  Same “autonomy disruption” is coming to many other areas
Autonomy V&V research (and practice) are really important
  ADS, autonomous ships, drones, assistive robots, …
  Consider contributing to it
Thank you
  Questions?